## Slide 1: Hyperspectral Imaging
Tapani Alakiuttu

## Slide 2
Sunlight consists of electromagnetic waves with many different wave lengths. Some of which we can see on rainbow as colours.
Have you ever observed the rainbow on a rainy day? This beautiful phenomenon where raindrops act as millions of small prisms makes an important characteristics of sunlight visible. Sunlight consists of electromagnetic waves with many different wavelengths, some of which in the rainbow we can see as colors.

## Slide 3: Content
Spectral Image Basics
Benefits of Spectral Imaging
Data Acquisition
Application Example
Other Applications
Video Content

## Slide 4: Spectral Image Basics

## Slide 5: The Electromagnetic Spectrum
We can see only very small part of it with our human eyes. Roughly between 400 and 750 nano meters.
On the lower end of the spectrum it extends to ultra violet and on the other end above red it extends to the infra red region of the spectrum
source: http://en.wikipedia.org/wiki/File:EM_spectrum.svg
author: Philip Ronan

## Slide 6: The Visible Spectrum – The World is Grey
If we have only one receptor in a visible range, we would see the world in different shades of grey.
We would not see different colour because we would not be able to differentiate different colours.
This would be a pretty boring world.

## Slide 7: The Visible Spectrum – Human Vision
Human visual system has three so called cones: a short cone (S), medium cone (M) and long cone (L).
Because of this three receptors we can see colours. Our brain brings this together.
Colour imaging sensor works pretty much the same way

## Slide 8: Spectral Imaging Basics - Overview
 | Monochrome | RGB | Multispectral | Hyperspectral | Spectroscopy
Spatial Information | yes | yes | yes | yes | no
Band Numbers | 1 | 3 | 2 - 10 | >10 | continuous
Spectral Information | No | limited | Yes | Yes | Yes
Chart: 

## Slide 9: Benefits of Spectral Imaging

## Slide 10: Benefits of Spectral Imaging
More information
Monochrome

## Slide 11: Benefits of Spectral Imaging
The more spectral data, the more information
Differentiation of material
Identification of material characteristics
  Determination of water content
Material composition

## Slide 12: Data Acquisition

## Slide 13: Hyperspectral Imaging Data Acquisition
Whiskbroom: Observe region pixel by pixel like using whiskbroom for cleaning floor and then extracting spectral information to line sensor. Not used much anymore.
Pushbroom: Observe one line at a time. Scan the sample line by line or the sample itself moves under this line. Nyperspectral data cube is build.
Staring: Take sample picture by picture with different filter.
Snapshot: With one shot spatial and spectral information. Requires quit sophisticated arrangement of mirrors and lenses.

## Slide 14: Application Example

## Slide 15: Application Example – 3 White Powders
Three different powders. Just by looking it is not possible to distinguish any.
Optotechnik und Bildverarbeitung (OBV)
Christian Günther
Frank Friehl
Prof. Dr. Heckenkamp
Source:

## Slide 16: Application Example – 3 White Powders
Optotechnik und Bildverarbeitung (OBV)
Christian Günther
Frank Friehl
Prof. Dr. Heckenkamp
Source:
Use Spectral Information
Chart: Remission [%]
Sodium
Carbonate
Sodium
Carbonate

## Slide 17: Application Example – 3 White Powders
Optotechnik und Bildverarbeitung (OBV)
Christian Günther
Frank Friehl
Prof. Dr. Heckenkamp
Source:
Sodium
Carbonate
Natron
Use Spectral Information
Chart: Remission [%]
Natron
Sodium
Carbonate

## Slide 18: Application Example – 3 White Powders
Optotechnik und Bildverarbeitung (OBV)
Christian Günther
Frank Friehl
Prof. Dr. Heckenkamp
Source:
Sodium
Carbonate
Natron
Powdered
Sugar
Use Spectral Information
Chart: Remission [%]
Natron
Sodium
Carbonate
Powdered Sugar

## Slide 19: Application Example – 3 White Powders
We have spectral data each of the material recorded.
Typically curves are
uninteresting in the
visible range but
come more
interesting in IR-range.
Sodium carbonate:
Spectrum is pretty
flat over wide range
of wave lengths
Natron: Flat in the
beginning but drops
suddenly after 1000 nm.
Sugar: Flat in the beginning
but more interesting
above 1000 nm.
Chart: Remission [%]
Natron
Monochrome
Sodium
Carbonate
Powdered Sugar
Sodium
Carbonate
Natron
Powdered
Sugar
X
Optotechnik und Bildverarbeitung (OBV)
Christian Günther
Frank Friehl
Prof. Dr. Heckenkamp
Source:

## Slide 20: Application Example – 3 White Powders
This is an interesting characteristics of many materials. We don't see very interesting spectral curve in the visible range but if we look at the infrared spectral range curves come very interesting and we start to be able to separate materials. This would not be possible if we just look the visible range.
If we look at those powders in regular monochrome sensor, as expected we can't differentiate them. All curves are pretty much flat in this region, which means that the sensor is quit saturated.
Chart: Remission [%]
Natron
Monochrome
Sodium
Carbonate
Powdered Sugar
Sodium
Carbonate
Natron
Powdered
Sugar
X
Optotechnik und Bildverarbeitung (OBV)
Christian Günther
Frank Friehl
Prof. Dr. Heckenkamp
Source:

## Slide 21: Application Example – 3 White Powders
If we take a colour imager and try to differentiate the powders with three RGB-filters, we still not see any distinguish possible.
Sodium
Carbonate
Natron
Powdered
Sugar
X
Optotechnik und Bildverarbeitung (OBV)
Christian Günther
Frank Friehl
Prof. Dr. Heckenkamp
Source:
Chart: Remission [%]
Natron
Powdered Sugar
Color (RGB)
Sodium
Carbonate

## Slide 22: Application Example – 3 White Powders
Sodium
Carbonate
Natron
Powdered
Sugar
Optotechnik und Bildverarbeitung (OBV)
Christian Günther
Frank Friehl
Prof. Dr. Heckenkamp
Source:
Chart: Remission [%]
Natron
Sodium
Carbonate
Powdered Sugar
Consider Infrared

## Slide 23: Application Example – 3 White Powders
If we take short wave infrared camera SWIR-camera, we hope to be able to distinguish them, but it is not possible.
Reason for this is that at the lower part of SWIR all signals are very high. All three substances are able to saturate the signal.
What can we do now?
SWIR
Chart: Remission [%]
Natron
Sodium
Carbonate
Powdered Sugar
SWIR
X
Optotechnik und Bildverarbeitung (OBV)
Christian Günther
Frank Friehl
Prof. Dr. Heckenkamp
Source:
Sodium
Carbonate
Natron
Powdered
Sugar

## Slide 24: Application Example – 3 White Powders
We take a very narrow bandpass at 1650 nm with width only 35 nm.
Suddenly the picture changes
Chart: Remission [%]
SWIR
ü
Optotechnik und Bildverarbeitung (OBV)
Christian Günther
Frank Friehl
Prof. Dr. Heckenkamp
Source:
Sodium
Carbonate
Natron
Powdered
Sugar
SWIR
Choose bandpass filter

## Slide 25: Application Example – 3 White Powders
We are now able to distinguish the three powders quit clearly.
Sodium carbonate has still quit strong signal and is quit saturated.
Powder sugar is somewhere between the two other substances, we see as grey.
Natron drops a lot and is seen as black.
You don't always need to observe the whole spectrum. Sometimes it can be enough if you know exactly what you want to do the substances you want to separate it is possible to use just one filter.
SWIR
ü
Optotechnik und Bildverarbeitung (OBV)
Christian Günther
Frank Friehl
Prof. Dr. Heckenkamp
Source:
Sodium
Carbonate
Natron
Powdered
Sugar

## Slide 26: Sometimes a filter is all it takes
You don't always need to observe the whole spectrum. Sometimes it can be enough if you know exactly what you want to do the substances you want to separate it is possible to use just one filter.
Depending on task, one filter can be enough
Can be a small and robust solution for easy integration
A hyperspectral solution reduced to one relevant bandpass
SWIR
ü
Optotechnik und Bildverarbeitung (OBV)
Christian Günther
Frank Friehl
Prof. Dr. Heckenkamp
Source:
Sodium
Carbonate
Natron
Powdered
Sugar

## Slide 27: And sometimes a multi/hyperspectral solution is require
Spectral curves of different plastics. Here it would not possible to use just one filter to differentiate. Curves are too similar. Here we could use for example seven filters and we could be able to distinguish quit many of the plastics.
It's always very specific how many filters are needed.
Wavelength [nm]
Spectral Remission [%]
Identification of recyclable plastics
Optotechnik und Bildverarbeitung (OBV)
Frank Friehl
Prof. Dr. Heckenkamp
Source:
Separation of Recyclable Plastics

## Slide 28: Other applications
Food sorting
Detection ripeness
Detection of impurities, foulness
Recycling
Separation of plastics
Waste separation
Separation of building materials
Agriculture/Farming
Detection of moisture content
Detection of nutriens

## Slide 29: Other applications
Aerial sensing
Mineralogy
Reconnaissance
Space exploration

## Slide 30: Video Content

## Slide 31: Video content
Multispectral Camera Technology by Spectral Devices Inc.
Multi- and hyper-spectral imaging by Mittuniversitetet

## Slide 32: Video Content
Introduction to Hyperspectral Remote Sensing by NEON Science
Multispectral and Hyperspectral Imaging for Plant Science by Analytik Ltd

## Slide 33: Video Content
How Specim line scan hyperspectral cameras work
What is hyperspectral imaging - Tutorial

## Slide 34: Video Content
What Hyperspectral Imaging provides - Tutorial
How to to know the right wavelength range

## Slide 35: Video Content
How to record data with hyperspectral camera - Tutorial
Sorting food with hyperspectral imaging

## Slide 36: Video Content
Sorting plastics with hyperspectral imaging
How to to know the right wavelength range